## Slide 1
PEERLINK
OFFLINE MESH COMMUNICATION SYSTEM
TEAM MEMBERS
Satyajeet Chavan
Yashraj Pawar
Ketan Gunjal
Kalyani Chalke
An offline, internet-free peer-to-peer messaging system using an ESP32 microcontroller as a portable Wi-Fi relay hub for Android devices.
Android
ESP32
Jetpack
UDP Mesh

## Slide 2
PEERLINK
An offline, internet-free peer-to-peer messaging system using an ESP32 microcontroller as a portable Wi-Fi relay hub for Android devices.
Android
ESP32
Jetpack
UDP Mesh
PEERLINK
OFFLINE MESH COMMUNICATION SYSTEM

## Slide 3
MOTIVATION
The Problem
🌐
Internet Dependency
All popular messaging apps rely on cloud servers and active internet connectivity to exchange messages.
🚫
Dead Zones
Remote areas, disaster zones, underground venues, and events often have no cellular signal or Wi-Fi infrastructure.
🔒
Privacy & Surveillance
Server-based messaging exposes messages to third-party cloud providers, creating privacy and security concerns.
💡 The Need: A simple, infrastructure-free communication method that works with just a small device and smartphones.

## Slide 4
SOLUTION
Introducing PeerLink
PeerLink transforms an ESP32 microcontroller into a portable Wi-Fi relay hub. Nearby Android phones connect to it and can chat with each other — completely offline, no SIM card, no internet, no server. • Works anywhere — even in remote areas • No registration, no accounts, no cloud • ESP32 costs under ₹400 and runs on a phone charger • End-to-end local network
ESP32 Acts As:
• Wi-Fi Access Point (hotspot) • UDP packet relay / router • Client registry & tracker • Presence broadcaster

## Slide 5
SYSTEM DESIGN
Architecture Overview
Android App
Sender
→
WifiNetworkSpecifier
Auto-connects
→
ESP32 Relay
Routes port 8888
→
Android App
Receiver
EspConnector
Auto-joins PeerLink Wi-Fi using APIs
UdpChat
Sends/receives JSON packets on UDP 8888
MeshService
Android Foreground Service orchestration
Room DB
Persists chat history locally

## Slide 6
HARDWARE LAYER
ESP32 Relay Firmware
• Wi-Fi AP Mode — Broadcasts SSID PeerLink_XXXX • UDP Server on port 8888 — Listens and routes • Client Registry — Tracks all connected devices • Presence Broadcast — Announces relay every 2s • Client Timeout — Removes inactive devices (30s) • LED Indicator — GPIO 2 blinks on activity
Arduino C++
ArduinoJson
void loop() { int packetSize = UDP.parsePacket(); if (packetSize) { String type = json["type"]; if (type == "chat") { routePacket(json["payload"], json["to"]); blinkLED(GPIO_2); } } checkClientTimeouts(); }

## Slide 7
ANDROID LAYER
Android Application
🔌
EspConnector
Uses Android's WifiNetworkSpecifier API to connect to hotspot networks via Kotlin callbackFlow.
📦
UdpChat
Manages DatagramSocket on port 8888 for UdpPacket objects. Uses Coroutines & MutableSharedFlow.
⚙️
MeshService
Foreground Service staying alive in background. Orchestrates DB and state flows.
🗄️
Room Database
Persists MessageEntity records locally. UI observes via a Flow<List<MessageEntity>>.

## Slide 8
PEERLINK
USER INTERFACE
App Screen Flow
Splash Screen
Brand intro
→
Permission
Wi-Fi, Location
→
Discovery
Connecting
→
Device List
Shows peers
→
Chat Screen
Messaging
Jetpack Compose
Declarative UI with Material 3, reactive state.
Navigation
Type-safe navigation with NavHost.
Dark Theme
Black background with white bubbles.

## Slide 9
DEEP DIVE
Message Data Flow
// 1. User taps Send → ViewModel → MeshService fun sendMessage(toPeerId: String, content: String) { val packet = UdpPacket(type="chat", from=myDeviceId, to=toPeerId, payload=content) database.messageDao().insertMessage(localMsg) // Save locally first udpChat.sendMessage(packet) // Send over UDP → ESP32 router } // 2. ESP32 receives packet → looks up target device IP → forwards // 3. Receiver's UdpChat emits via SharedFlow → MeshService handles when (packet.type) { "chat" -> database.messageDao().insertMessage(incomingMsg) "clients_list" -> _serviceState.update { it.copy(peers = parsedPeers) } } // 4. Room DB change → Flow emits → Compose UI auto-recomposes
Coroutines
StateFlow
Room Flow

## Slide 10
01101001 01101110 01101011
MULTI-HOP ROUTING
ESP-TO-ESP PACKET FORWARDING
DATA
DATA
DATA
📱 Sender
⚡ ESP32 Node A
⚡ ESP32 Node B
⚡ ESP32 Node C
📲 Receiver
When the Receiver is out of direct range, the protocol dynamically routes the payload through intermediate ESP32 nodes (Node A → Node C). Inactive nodes (Node B) remain on standby to self-heal the network if a primary node fails.

## Slide 11
TECHNOLOGY
Technology Stack
📱
Android / Kotlin
Jetpack Compose · Navigation · ViewModel · Room DB · Foreground Services
⚡
Embedded / C++
ESP32 Arduino SDK · WiFi.h · WiFiUdp.h · ArduinoJson
🌐
Networking
WifiNetworkSpecifier API · UDP Datagrams · Port 8888 · Broadcast routing
NO
Internet Required
<₹400
Hardware Cost
8888
UDP Port
2s
Broadcast Interval

## Slide 12
LITERATURE SURVEY
Related Work & Prior Art in Offline Peer-to-Peer Communication Systems
Meshtastic (2019) — LoRa Mesh
Open-source LoRa-based mesh network for off-grid communication. Uses radio modules (not Wi-Fi); range up to 10 km but requires dedicated LoRa hardware per device and has lower bandwidth than Wi-Fi UDP.
Gap: Requires specialised LoRa hardware; PeerLink uses smartphone Wi-Fi directly.
Briar (2021) — Tor/Bluetooth P2P
Secure messaging app using Tor, Bluetooth, or Wi-Fi Direct. Designed for activists. Requires both peers to be online simultaneously; no persistent relay node for store-and-forward.
Gap: No centralised relay; PeerLink’s ESP32 acts as always-on hub for asynchronous delivery.
GoTenna Mesh (2017) — BLE/RF Mesh
Proprietary hardware dongle using 900 MHz RF for off-grid texting. Requires purchasing a $179 device per user; not universally available and not open-source.
Gap: Costly & closed. PeerLink uses a <₹400 ESP32 with open firmware and standard Wi-Fi.
Wi-Fi Direct (IEEE 802.11) — Ad-hoc
Standard that allows device-to-device Wi-Fi without an AP. Android fragmentation, complex group-owner negotiation, and no multi-hop routing limit practical deployability.
Gap: PeerLink avoids OS-level Wi-Fi Direct; ESP32 AP provides a stable, routable subnet for all devices.
💡 PeerLink’s Novelty: Unlike prior work, PeerLink combines an ultra-low-cost ESP32 Wi-Fi AP with a standard Android Kotlin app (no custom hardware needed by users), providing a simple, open, and deployable offline mesh chat system.
System Hardware Needed Internet-Free Open Source Multi-hop Cost
Meshtastic LoRa Module Yes Yes yes ~$30-60
Briar None (uses phone) Yes Yes No(not automatic) Free
GoTenna Mesh Proprietary RF dongle Yes No yes ~$179
Wi-Fi Direct None Yes Yes No Free
PeerLink (Ours) ESP32 (~₹400) Yes Yes Yes ~₹400

## Slide 13
IMPACT & ROADMAP
Use Cases & Future Scope
🎯 Real-World Use Cases • Disaster Relief — Communication when towers are down • Remote Expeditions — Trekking, camping, mountaineering • Event Management — Large venues with poor connectivity • Underground Facilities — Mines, bunkers, basements • Campus / Office — Private local-only communication
🚀 Future Enhancements s • End-to-end message encryption (AES/RSA) • File / image transfer support • Group chat & broadcast channels • iOS client application

## Slide 14
END OF PRESENTATION
Thank You
PeerLink — Connecting People, Offline.
📱
Android (Kotlin)
⚙️
ESP32 Firmware
💬
Offline Mesh
Built with Kotlin · Jetpack Compose · ESP32 Arduino · UDP Networking